## Slide 1: The Vision Pipeline: From Pixels to Real-World Engineering Solutions
Guide by Jeni Gracia R C
Logesh S 192525023
YOUR LOGO

## Slide 2: Image Formation & Fundamentals
The Physics of Capture: Lenses bend light rays to project a 3D real-world scene onto a flat 2D sensor plane (Perspective Projection). Sensor Electronics: Charge-Coupled Devices (CCD) or Complementary Metal-Oxide-Semiconductor (CMOS) sensors convert photon energy into electrical voltages.
The Pixel Grid: Images are stored as 2D digital matrices \(f(x,y)\), where \((x,y)\) represents spatial coordinates and \(f\) represents light intensity. Colour Representaton: Light is split into discrete colour channels like RGB (Red, Green, Blue) for display, or HSV (Hue, Saturation, Value) for easier computer processing.
Notes: It is a closed-loop technological pipeline that transforms real-world physical light into actionable digital intelligence.

## Slide 3: Digitalization: Sampling & Quantization
Spatial Sampling: The continuous real-world scene is divided into a discrete grid of pixels; this dictates the physical spatial resolution.
The Nyquist Limit: Sampling frequencies must double the highest spatial frequency of the scene to prevent aliasing (distorted, jagged artifacts).
Intensity Quantization: Continuous voltage values are mapped into discrete integer gray levels based on the system's bit depth (e.g., 8-bit depth yields \(2^8 = 256\) levels).

## Slide 4: Interpretation: Computer Vision Processing
Low-Level Processing: Mathematical filters remove sensor noise (Gaussian blur) and highlight sudden intensity changes to map structural outlines.
Feature Extraction: Mathematical algorithms isolate robust mathematical landmarks, textures, or keypoints within the pixel matrix.
Object Segmentation: Pixels with matching intensities or boundaries are grouped together to isolate distinct objects from the background.
High-Level Recognition: Machine learning models classify the grouped pixels, turning raw matrix data into actionable labels

## Slide 5: THANK YOU
Logesh S 192525023